## Slide 1
Digital Image Enhancement
Day-2 : March 14, 2015

## Slide 2
Image Enhancement
Topics today: Pixel Processing
Brightness vs. Contrasts
Modify brightness:
  Histogram Sliding towards Right
  Histogram Sliding to Left
To Intensify Contrast of an Image
  Histogram Stretching : Procedure, Limitations
  Histogram Equalization
Logarithmic Transforms
  Gamma Correction
  Log Transform

## Slide 3
Brightness vs. Contrast

## Slide 4
Brightness vs. Contrasts Contd.
To change Brightness of an Image, change the intensity of its pixels
∴ g(x,y) = f(x,y) ± θ ⇨ Brightness of the image is uniformly modified,
                if θ be constant , viz. = =0 , ∀ (x,y)
To change Contrast of an Image, widen the pixels’ gray level band
∴ g(x,y) = ψ [f(x,y)] ⇨ Contrast modification with ψ if
                histogram of the output image is wider than the histogram of the original image
ψ is intensification operator that can have different implementations

## Slide 5
Increasing Brightness (Slide-to-Right)
To increase Brightness of an Image, increase the intensity of its pixels
∴ g(x,y) = f(x,y) + θ ⇨ Brightness of the image is uniformly increased,
                if θ>0 be constant , viz. = =0 , ∀ (x,y)
Brightening means to slide to right

## Slide 6
Reducing Brightness (Slide-to-Left)
To reduce Brightness of an Image, reduce the intensity of its pixels
∴ g(x,y) = f(x,y) - θ ⇨ Brightness of the image is uniformly reduced,
                if θ>0 be constant , viz. = =0 , ∀ (x,y)
Darkening means to slide to Left

## Slide 7
g(x,y)= * (2 K -1)
Intensify Contrast: Histogram Stretching
Assume an image :
8-bit Grayscale
Minimum intensity of the pixels= 112
Maximum intensity of the pixels = 180
∴ k=8, = 180, = 112
∴ g(x,y)= *255
= *255
It fails to enhance the contrast in the following situation:
An image whose minimum intensity=0, maximum intensity =255
g(x,y)= *255 =

## Slide 8
Intensify Contrast: Histogram Stretching Examples
Compare Histograms

## Slide 9
Histogram is Stretched: Example
Grayscale band stretched

## Slide 10
Logarithmic Transformations
Types of Logarithmic Transformations:
  Log Transform
  Gamma Transform (Inverse Log Transform)
s= | > 0 ∧ s<255
s=g(x, y)  Output Image Pixel Intensity
r= f(x, y)  Input Image Pixel Intensity
∵ 0≤s≤255 [For 8-bit Images]
∴ ≤
Instead of r, we take
Otherwise, if intensity of the pixel (r) be zero, we end up with -∞
Instead of r, we take
Any base of Logarithm may be used as it only needs to change value of

## Slide 11
Properties and Utility of Log transform
s= ⇒ = ⇒ The curve is steep (has high and linearly slope) for small values of ; but for larger values it becomes less steep but more widened.
∴the dark pixels in an image are expanded more and high pixel values are compressed